ManMon

MSBD Data Center Monitoring System

# 1. Introduction
ManMon is Data Center monitoring system of Mangrove Systems Bangladesh. It will monitor the data center environment and control relay switch.
# 2. Overall Architecture

ManMon

Instructions

Status

ManMon Server / Control Unit / Data / Center

Environment Status

Raspberry Pi

On/Off

Relay

Noise

Humidity

Light

Lamp
Temperature

Figure 1: ManMon Component Architecture
# 3.Controller Unit
## 3.1 Setup Raspberry Pi Environment
Installing Raspbian OS
Raspberry Pi OS (32-bit) with desktop and recommended software
version : Auigust 2020
Kernel version : 5.4
Step 1: Download Raspbian
Step 2: Unzip the file
Step 3: Write the disc image to your microSD card using Imager (Raspbian Imager)
Step 4: Put the microSD card in your Pi and boot up

Install Python3

#sudo apt update

#sudo apt install python3

Install pip3

#sudo apt-get update

#sudo apt-get -y install python3-pip

Install RPi.GPIO Python Library

#wget https://pypi.python.org/packages/source/R/RPi.GPIO/RPi.GPIO-0.5.11.tar.gz
#tar -xvf RPi.GPIO-0.5.11.tar.gz
#cd RPi.GPIO-0.5.11
#sudo python setup.py install
Reference: https://www.raspberrypi-spy.co.uk/2012/05/install-rpi-gpio-python-library/

Install PIGPIO Library

#sudo wget https://github.com/joan2937/pigpio/archive/master.zip
#unzip master.zip
#cd pigpio-master
#sudo make
#sudo make install
Reference : http://abyz.me.uk/rpi/pigpio/download.html

after installing pigpio library we need to start the pigpio service,

#sudo pigpiod

every time, raspberry pi restarts we must need to start this service

Install smbus

#sudo apt-get update

#sudo apt install python3-smbus

Install I2C

#sudo apt-get update

#sudo apt-get install i2c-tools

If this error occurs
Error:Could not open file `/dev/i2c-1': No such file or dire
https://www.raspberrypi.org/forums/viewtopic.php?t=115080

Note: set

Install Cherrypi Server

#git clone https://github.com/cherrypy/cherrypy
#cd cherrypy
#python3 setup.py install

## 3.2 Tools and Components
We are going to use
1. Raspbian as OS of raspberry pi 4 Model-B
2. Thonny IDE
3. cherrypi server
4. spring boot(Back End),AngularJs(Front End)
Metric	Purpose	Sensor/ / Component	Model (Clone)	Unit Price	No. of Units	Price
Humidity,Temperature	Receive Humidity	Humidity Sensor * 3	AM2301	800	2	300
Noise	Receive Sound	Sound Sensor	FC-04	650	1	650
Camera*	Visualize Data Center	Raspberry Pi Cam	ROB-00350	IP?
Light	Sense Light Intensity	Light Sensor	BH1750	53	3	160
Lamp	Environment Lighting	LED Bulb	20 watt	300	1	300
Relay	Convert DC signal to AC	Relay Switch / (4 Channel)	MIS-00362	200	2	400
Raspberry Pi 4	Server Computer	Raspberry Pi 4(4GB)	DEV-00110/ M-B	6300	1	6300
Memory card	Hard disk Raspberry	64GB	SanDisk class10	1800	1	1800
Micro HDMI to HDMI	Raspberry Pi 4 to connect to a HDMI monitor	Cable	C&C-00236	385	1	385
Casing	https://www.electronics.com.bd/Acrylic-Case-for-Raspberry-Pi-4-Model-B-Raspberry-Pi-Case-with-Cooling-Fan-Black-and-Clear-electronics-com-bd		Raspberry Pi 4	446	1	446
Soldering	Soldering iron-60W (tatal)		TOL-00018
	ran
	rojon
Jumper cables	M2F			40
	M2M			40
	F2F			40
Bread board
PCB		20 yard
Raspberry Pi 4 / power adapter			MIS-00490
AC cables
Ethernet Cable		1 piece
Glue gun	gluing	1
Tatal holder	To hold tatal	1
Cutter	Cutting wires	1
Tester		1
Plus		1
Screw driver	Screwing	2

## 3.3 Components which actually used in ManMon:
Sensor	Model
Humidity Sensor	AM2301
Sound sensor	FC-04
Light sensor	BH1750

## 3.4 Components which were recommended and also available as backup:
Sensor	Model
Humidity Sensor	AM2301,DHT22,DHT11
Sound sensor	FC-04
Light sensor	BH1750

## 3.5 Controller Unit and It’s Responsibilities
A. Publishes and Receives Environment Data and Instructions to and from ManMon Server
I. Tasks
- Receives Instructions From ManMon.
- Sends Environment Data to ManMon
II. Technical
- Programming Language : Python3.
- Communication : Web Socket
- Data Format : JSON

B. Receives and Sends Instructions and Environment Data from and to Raspberry Pi
I. Tasks
- Receives Environment Data from Raspberry Pi.
- Sends Instructions to Raspberry Pi
II. Technical
- Module : Raspberry Pi 4
- Communication : Serial port
- Sensors: Humidity, Noise , Temperature , Camera , Light
-Device : Lamp
## 3.6 Circuit Diagram

## 3.7 Library Matrix

Sensors	Rpi.GPIO Library	PIGPIO	DHT22 Library	Smbus Library
Humidity and Temperature Sensor	x	√	√	x
Light Intensity sensor	x	x	x	√
Sound Sensor	√	x	x	x
Relay	√	x	x	x

Sensors:

1. Humidity Sensor(AM2301) x 1
2. Light Intensity Sensor(BH1750) x 1
3. Noise Sensor x 2 (Reference :https://bdspeedytech.com/index.php?route=product/product&product_id=1399&search=sound+sensor )
Sensors:
1. 4-channel Relay x 1

# 4. ManMon Agent
## 4.1 Environment Setup

Tools we need to setup:
1. OpenJDK 14.0.1
2. Netbeans 12.0
3. Maven 3.6 or higher

OpenJDK
1. Download openjdk-14.0.1_linux-x64_bin.tar.gz
2. Extract ‘openjdk-14.0.1_linux-x64_bin.tar.gz’
3. Move ‘openjdk-14.0.1’ folder to /usr/lib/jvm
4. Set JAVA_HOME and PATH with this following command
    $ export JAVA_HOME=/usr/lib/jvm/jdk-14.0.1
  $ export PATH=$JAVA_HOME/bin:$PATH
5. Check JDK version
  $ java -version
Download Ref: https://www.oracle.com/java/technologies/javase/jdk14-archive-downloads.html
Netbeans
1. Download Apache-NetBeans-12.1-bin-linux-x64.sh
2. Install Netbeans
References: https://netbeans.apache.org/download/nb121/nb121.html
Maven
sudo apt install maven
## 4.2 Components Definition
Web Socket: The Web Socket protocol, provides a standardized way to establish a full-duplex, two-way communication channel between client and server over a single TCP connection.

Web Socket Endpoint: /portfolio is the HTTP URL for the endpoint to which a Web Socket (or SockJS)
client needs to connect for the Web Socket handshake.

STOMP: Simple Text Oriented Messaging Protocol. It is designed to address a minimal subset of commonly used messaging patterns. Although STOMP is a text-oriented protocol, message payloads can be either text or binary.
Clients can use the SEND or SUBSCRIBE commands to send or subscribe for messages, along with a destination header that describes what the message is about and who should receive it.

Messages Mapping: STOMP messages whose destination header begins with /app are routed to @MessageMapping methods in @Controller classes.

Topic: Whose destination header begins with /topic. /topic is the built-in message broker for subscriptions and broadcasting and route messages. Client SUBSCRIBE to a broker to get published/broadcasted messages by the broker.

Fetch: In this case Fetch means data retrieve from the application database. We do this using HTTP.GET request method.

Response: In response of HTTP.GET request we get a response which is our desired data.

Scheduler: Scheduler is a Spring Boot @Component Class. Where we can execute a method after a fixed time continuously.

Sensor-Controller: Sensor-Controller is simple HTTP-Server, built using Python3 CherryPi framework. This server receives HTTP request to retrieve environment status from the sensor and also execute device control instructions given by the monitor admin.

References:
1.https://docs.spring.io/spring-framework/docs/current/spring-framework-reference/web.html#websocket
## 4.3 ManMon Communication Layers

## 4.4 Request Mapping

Front-End «» Agent Request Mapping
SN	Frontend «» Agent	Type	Response	Description
				Purpose	Steps
	/topic/sensorinfo	Subscribe / (initial page load)	/sensorinfo	Scheduled sensor info in every 10 second	- Agent sends http request to sensor controller and in response get current environment status / - Agent add noiseLevel and sensors min-max status with environment status and publish to clients
	/thirtyday_min_max	GET / (initial page load)	/current_date_min_max	Fetch Thirty day min-max value of sensors	- Agent fetch last thirty days min-max value of sensors from DB and sends to client
	/threshold	GET / (initial page load)	/threshold	Fetch Sensors threshold value	- Agent fetch threshold value of sensors from DB and send to clients
	/initial_sensorinfo	GET (initial page load)	/initial_sensorinfo	Fetch last 15 minutes sensorinfo to client	- Agent fetch last 15 minutes sensorinfo from DB sends to client
	/specific_hour_sensorinfo	GET / (initial page load or user request)	/specific_hour_sensorinfo	Fetch specific hours sensorinfo to client	- Agent fetch specific date-hour sensorinfo from DB and sends to client
	/setlampup	GET	/setlampup	Set Lamp on	- Agent sends http request to sensor controller and in response get Lamp status / - Agent sends Lamp status to client
	/setlampdown	GET	/setlampdown	Set Lamp off	- Agent sends http request to sensor controller and in response get Lamp status / - Agent sends Lamp status to client
	/setdehumidifierup	GET	/setdehumidifierup	Set Dehumidifier on	- Agent sends http request to sensor controller and in response get Dehumidifier status / - Agent sends Dehumidifier status to client
	/setdehumidifierdown	GET	/setdehumidifierdown	Set Dehumidifier off	- Agent sends http request to sensor controller and in response get Dehumidifier status / - Agent sends Dehumidifier status to client

Agent «» Sensor-Controller Request Mapping
SN	Agent «» Sensor	Type	Response	Description
				Purpose	Steps
	/sensorinfo	GET	Environment status JSON	Fetch environment status in every 10 second	- Scheduler sends http request in every 10 second to sensor-controller / - In response get Environment status
	/setlampup	GET	‘Relay for Lamp is set to On’	Lamp on	- Sends http request to sensor-controller / - In response get Lamp status
	/setlampdown	GET	‘Relay for Lamp is set to Off’	Lamp off	- Sends http request to sensor-controller / - In response get Lamp status
	/setdehumidifierup	GET	‘Relay for Dehumidifier is set to On’	Dehumidifier on	- Sends http request to sensor-controller / - In response get Dehumidifier status
	/setdehumidifierdown	GET	‘Relay for Dehumidifier is set to Off’	Dehumidifier off	- Sends http request to sensor-controller / - In response get Dehumidifier status

## 4.5 ManMon Future Development Plan

# 5. Manmon (Front-End)

## 5.1 Environment Setup

Tools we need to setup:
1. Node (Latest version)
2. VS Code

Node Installation :

nvm install node

If nvm is not installed on your machine then install nvm first

Installing nvm:

curl -o- https://raw.githubusercontent.com/nvm-sh/nvm/v0.35.3/install.sh | bash

VsCode Installation :

Download and Install
https://go.microsoft.com/fwlink/?LinkID=760868

# 6. Appendix
RPI.GPIO
Reference: https://www.raspberrypi-spy.co.uk/2012/05/install-rpi-gpio-python-library/
PIGPIO
Reference : http://abyz.me.uk/rpi/pigpio/download.html
OpenJDK
Download openjdk-14.0.1_linux-x64_bin.tar.gz
Netbeans
References: https://netbeans.apache.org/download/nb121/nb121.html